## Slide 1: From tree to boards
Wait wood is how expensive?

## Slide 2: Find a forest
Get permission to harvest
  You do not want the pointy end of “tree law”
Fun fact: “Jackson Oak” in Atlanta, GA
  Bonus, inheritance!
Best time is winter

## Slide 3: Find a tree
Not close to structures
Not rotted
  Windowmakers
  Standing dead trees OK
  Leave some for wildlife!
No twisted bark/grain
No lopsided limbs
  Unpredictable fall
Species of tree
Notes: If you are looking for firewood then fallen trees are best for this—just be sure to check for wood eating insects.

## Slide 4: Personal Protection Equipment
Safety pants!
Steel toed boots
Gloves (vibration!)
Eye protection
Ear protection
Hard hat
Hammer + wedges

## Slide 5: Choosing a chainsaw
Bar length
Gas vs electric
Notes: Fast and dangerous

## Slide 6: Using a chainsaw
Route of egress
  Falling los can kickback
  Fallen logs can roll
Spotter (safety)
Stance
  Stand to the side
  Firm grip
Starting
Cut with base of bar
Avoid dirt
Bar getting pinched

## Slide 7: Maintaining a chainsaw
Fuel mix
Sharpening
  Cross vs Straight cut
Chain tension
Safety chain brake
Notes: 2 stroke
Sharpening can be done yourself or at a rural hardware store
Tension: pulling chain away from middle of bar should JUST barely come out of the groove then snap back.

## Slide 8: Felling
Clear obstacles around tree
Pick a direction for tree to fall
  Beware lopsided limbs
Escape route
How to cut hinge

## Slide 9: Bucking
De-limb first
  Tree can roll
Sectioning into smaller pieces
  Tree can roll
Transporting sections

## Slide 10: “Alaskan” chainsaw mill
Attaches to your chainsaw
Extremely portable
  Easier to transport boards than a log
Height adjustable
  leave room for drying
Needs a “starter board”
Large wasteful kerf

## Slide 11: Drying
Stack with 1 inch wooden spacers
  Shims cause warping
  18 in apart
Covered top, open sides
Place in windy spot
1 year per inch thickness, roughly
Shrinkage will happen
Rough lumber

## Slide 12: Planing wood
Wood planer
Hand planer
Tablesaw Jig
Dimensional lumber

## Slide 13: References
Grandpa
“A Reverence for Wood” by Eric Sloane
Mr. Chickadee’s YouTube channel
YouTube in general
Notes: Grandpa can even be your spotter, or if you know neighbors (or me) you can take turns on the saw.

## Slide 14: Take a tree, leave a tree
If doing large scale lumbering then replant!

## Slide 15: Q&A / Fin

## Slide 16: Choosing a tool
Personal Protection Equipment
Chainsaw
Axe
Manual saw

## Slide 17: Choosing an axe
More than one type of axe
  Broad
  Adz
  Maul
  Felling
  Boy’s
Fiberglass vs wood handle
Handle length
Head material quality
Sharpening
Notes: Slow and dangerous
Work off the isolation weight

## Slide 18: Manual saw
Boring
One or two or variable person saws
Cross cut vs straight cut
Sharpening
Notes: Slow and safe

## Slide 19: Hewing
Log dog